## Slide 1: Nice To Meet You
Group 7
Ambient Intelligence Course
A.Y. 2017-18
https://ami-2018.github.io/NTMY/

## Slide 2: Introduction
NTMY team

## Slide 3: What is NTMY
NTMY is an Ambient Intelligence system that aims to help students in university residences to meet new friends by letting the users organize thematic events.
The goal of the project is to build a system that can be used in university residences to smartly organize events in order to let people meet others with the same interests. For this purpose, it makes use of different kinds of electronic devices such as PCs, mini computers, smartphones and wearables, all of which contribute to solve different problems that can be experienced during the organization of an event.
- Taken from Vision and Goal

## Slide 4: System architecture

## Slide 5: NTMY Team
Alessio Ciarcià
SW developer
Matteo Corain
SW developer
Andrea Cossio
HW developer
Raffaele Tuzzo
SW developer
Wear app
Panel app
Server app
Client app
Smartphone app
Panel design
Panel app

## Slide 6: Server architecture
Matteo Corain

## Slide 7: Server main functions
Data storage
The server stores all the data regarging the users, the events and the rooms
Events allocation
The server is capable of the smart allocation of the rooms based on the events’ characteristics
API interface
The server presents an HTTP REST API-based interface to communicate with the other components of the system

## Slide 8: Data storage
Uses Python SQLAlchemy support library, with SQLite as the database backend
Manages data about users, rooms, events and their relationships
The data model is organized in several subpackages, all containing classes whose objects are mapped from and to the database

## Slide 9: Data model
Main components:
Package standard:
  User, Room, Event
  Category, Facility
Package relationships:
  UserConnection, EventParticipant
  EventFacility, RoomFacility
  EventCategory, UserInterest
Package map:
  Node, Edge
Package media:
  Channel, Playlist

## Slide 10: Events allocation
Generates the daily schedule matching rooms and events
Uses a brute force optimization method
It is capable of optimizing different target functions
Makes sure that events fit the rooms and don’t overlap
Run asynchronously in a separated thread

## Slide 11: Allocation process
The allocate_rec function generates all the permutation of n integers (being n the number of the rooms, considering also 0 as the special value meaning «the event will not be scheduled») in k position (being k the number of the daily events) via recursion techniques
Once a permutation has been calculated, a DailySchedule object is generated; if the schedule is valid (events fit the assigned rooms and do not overlap), it is passed to the TargetFunctionsSet object
The TargetFunctionsSet calculates the value of all the TargetFunction objects for the given schedule and compare them with the ones of best solution found until that point
If the schedule is better, the best solution is updated and, at the end of the process, the best daily schedule overall is produced

## Slide 12: API interface
Uses Flask as the HTTP server
Exposes APIs to access data about users, rooms, events, media contents, graph nodes
Access to data is restricted only to registered users
Designed using the Google Developers guidelines

## Slide 13: Main routes
/login
/users
/rooms
/events
/schedule
/media
/map
The full documentation is on the Github repository

## Slide 14: Room clients
Matteo Corain

## Slide 15: Room clients activities
Login into the server
Get the information on the next event
Set the lights with the events color
Set the music or TV player
Wait until the event is finished
Loop for the following event

## Slide 16: Used libraries
Requests
Login phase and server information exchanging
Subprocess
OMXPlayer management
Philips Hue control
Pafy
Youtube music playlist fetch
TV channels fetch

## Slide 17: Lights management
Philips Hue bulbs controlled via the HTTP REST API
All the interaction takes place in a LightManager object
The color is obtained from the events’ schedule
Possible to convert a RGB color with the rgb_to_hue function
Possible to set all or a subset of the lights in the room

## Slide 18: Media management
OMXPlayer is used as the player backend for its compatibility with Raspberry Pi boards, running as a subprocess
The interaction takes places in a Player object
TV channels (RAI) are fetched in m3u8 files faking the User Agent to the one of a normal browser
Music playlists are fetched in m3u8 files through pafy library

## Slide 19: NTMY Android app
Andrea Cossio

## Slide 20: NTMY Wear app
Alessio Ciarcià

## Slide 21: Step 1: Design
Once opened it shows:
User’s name and surname
Event’s informations
Event’s related color in the background.

## Slide 22: Step 2: Load data
When user runs the wear app:
Wear sends a message to the phone in order to obtain the data
If the phone is connected to the server (user logged) sends back the requested data and the wear update the layout with real data.
Otherwise if the phone can’t reach the server, the wear will shows the default data ( previous slide ).

## Slide 23: Step 3: Handshake Detection
An handshake is here considered as a significant acceleration on wear’s Y axis.
The detection must be calibrated in order to not associate ordinary user’s movement to handshake.
On the other hand it must be sensitive enough not to lose any handshake
Assumptions & limitations:

## Slide 24: Step 3: Handshake Detection
When an handshake is detected:
Check if is passed enough time since the last one.
Send a message to the phone.
The phone searches the other smartwatch (note: smartwatches only have «always detectable» enabled) and if it is found, phone sends back to the wear the data of detected user (smartwatch).
The phone will show a toast containing the user’s fullname.
Smartwatch instead will show user’s pic and fullname (right photo)
Algorithm:

## Slide 25: Routing
Alessio Ciarcià

## Slide 26: Step 1: Design college model
Our imaginary college has been designed taking into account that:
Bookable rooms are not all in the same location
The streets do not form a perfect grid so that the routing prediction is not trivial.

## Slide 27: Step 2: Graph model
From the college model was built a graph over it:
There are 32 nodes covering almost all the crossroads.
In each nodes there is a direction panel.
A node has at most 4 edges => 4-directions panel

## Slide 28: Step 3: Programming
The database contains two tables, one for nodes and another for edges.
Each node has a string identifier, coordinates and panel orientation (since not all the crossroads have orthogonal intersections or not all the streets are aligned with cardinal axes.
Each edge tuple contains the two nodes id and the length of associated stretch of road
Process: Database creation.

## Slide 29: Step 3: Programming
Load edges and nodes data from the server.
With the use of Networkx module create the graph and add all nodes and edges.
Process: Graph creation.

## Slide 30: Step 3: Programming
To generate the direction from start node to the destination one is used the Dijkstra algorithm in order to obtain the best path and return the exit related to the next node in this path.
The exit point is obtained by calculating the vector corrisponding to the edge and then the angle with arctan function. To each exit corresponds an equal portion of the entire corner, based on the equation:
    Exit point n.b the result is rounded to the nearest.
Process: Strategy.

## Slide 31: Smart Panels
Raffaele Tuzzo

## Slide 32: Goal
To realize the Smart Road Sign:
We need a configuration to sign all the 4 cardinal direction
2. We want to set a color to the arrow, according to the event’s color

## Slide 33: Ideas
We can use 8 Leds, set up in a rhombus scheme to represent the 4 possible arrows.
To set every possible color we can use RGB Leds, setting a color by the right combination of this 3 colors.
Leds
c
Anode
Cathode R
Cathode G
Cathode B

## Slide 34: How to drive leds
We used a Raspberry PI ( B model ) as Micro-controller.
To drive a single led we chose a buffer in an Open Emitter configuration, using npn transistors.
Now we can switch a led, the npn works in saturation (ON) and in interdiction (OFF) mode.
Rb
Rb = 1 Kohm
( it is used as protection )

## Slide 35: Color set up
To change color we need to change the brightness of each led thank to the provided power from micro-controller.
Pulse Width Modulation ( PWM ) : we vary the Duty Cycle of the square waveform to change the brightness.
µ controller
NPN used as buffer in Open Collector configuration
Raspberry PI pinout: - VOH = 3.3 V
- VOL = 0 V
.
T
Th

## Slide 36: General Configuration
We have in total 24 leds to drive, so we need 24 pins, 1 pin as supply and 1 pin for the ground. It’s too much!
We can use a Scanning Multi-LEDs Interface:
We set up leds in a matrix configuration 8 x 3
8 Rows: npn in OE buffer to switch leds ON/OFF
3 Columns: npn in OC buffer to drive pwm modulation
R
C

## Slide 37: General Configution

## Slide 38: Demo time!
NTMY team

## Slide 39: What you’ll see today
Event creation and joining
Room preparation
Directional panels
NTMY action